## Slide 1
Mean effective pressure
The mean effective pressure can be used as a parameter to compare the performances of reciprocating engines of equal size.
The engine with a larger value of MEP delivers more net work per cycle and thus performs better.

## Slide 2
OTTO CYCLE: THE IDEAL CYCLE FOR SPARK-IGNITION ENGINES

## Slide 3
Schematic of a two-stroke reciprocating engine.
The two-stroke engines are generally less efficient than their four-stroke counterparts but they are relatively simple and inexpensive, and they have high power-to-weight and power-to-volume ratios.
Four-stroke cycle
1 cycle = 4 stroke = 2 revolution
Two-stroke cycle
1 cycle = 2 stroke = 1 revolution

## Slide 5
Air enters the cylinder through the open intake valve at atmospheric pressure P0 during process 0-1 as the piston moves from TDC to BDC.
The intake valve is closed at state 1 and air is compressed isentropically to state 2. Heat is transferred at constant volume (process 2-3); it is expanded isentropically to state 4; and heat is rejected at constant volume (process 4-1).
Air is expelled through the open exhaust valve (process 1-0).
Work interactions during intake and exhaust cancel each other, and thus inclusion of the intake and exhaust processes has no effect on the net work output from the cycle.
However, when calculating power output from the cycle during an ideal Otto cycle analysis, we must consider the fact that the ideal Otto cycle has four strokes just like actual four-stroke spark-ignition engine.

## Slide 6
In SI engines, the compression ratio is limited by autoignition or engine knock.

## Slide 7
DIESEL CYCLE: THE IDEAL CYCLE
FOR COMPRESSION-IGNITION ENGINES
In diesel engines, only air is compressed during the compression stroke, eliminating the possibility of autoignition (engine knock). Therefore, diesel engines can be designed to operate at much higher compression ratios than SI engines, typically between 12 and 24.
1-2 isentropic compression
2-3 constant-volume heat addition
3-4 isentropic expansion
4-1 constant-volume heat rejection.

## Slide 8
Thermal efficiency of the ideal Diesel cycle as a function of compression and cutoff ratios (k=1.4).
Cutoff ratio
for the same compression ratio

## Slide 9
Dual cycle: A more realistic ideal cycle model for modern, high-speed compression ignition engine.
In modern high-speed compression ignition engines, fuel is injected into the combustion chamber much sooner compared to the early diesel engines.
Fuel starts to ignite late in the compression stroke, and consequently part of the combustion occurs almost at constant volume.
Fuel injection continues until the piston reaches the top dead center, and combustion of the fuel keeps the pressure high well into the expansion stroke.
Thus, the entire combustion process can better be modeled as the combination of constant-volume and constant-pressure processes.